## Slide 1
We introduced a projection-driven, patient-specific deep learning framework for CBCT motion compensation.
Our non-iterative method is fast, accurate, and robust to inter-fraction anatomical changes. It effectively suppresses motion artifacts, enabling the synthesis of high-quality static 3D and full 4D-CBCT datasets, paving the way for advanced adaptive radiotherapy.
Abstract
Projection-Driven Robust Motion Compensation for CBCT using a Patient-Specific Model Learned from Prior Scans
Yilin Shao1,3, Jingjing Dai3, Lei Deng3, XinKai Xu2, Jun Zhang4, Yaoqin Xie3, Xiaokun Liang3
1Department of Shenzhen University of Advanced Technology, Southern University of Science and Technology, Shenzhen, 518055, China
2CGN Medical Technology (mianyang) Co., Ltd
3Shenzhen Institute of Advanced Technology, Chinese Academy of Sciences, Shenzhen, 518055, China
4Department of Oncology, People’s Hospital of Longhua, Shenzhen, 518109, China
Respiratory motion artifacts severely compromise the diagnostic utility of Cone-Beam CT (CBCT). Motion-compensated (MoCo) reconstruction faces a critical trade-off: fast deformation vector field (DVF) estimation from prior scans can be inaccurate against anatomical changes, while accurate iterative methods are too slow for clinical workflows. We propose a learning-based MoCo framework to resolve this dilemma. It utilizes a deep neural network, trained patient-specifically on a prior 4D-CT, to rapidly and directly infer DVFs from 2D projections. This non-iterative approach leverages a learned motion model to ensure both efficiency and robustness against inter-fractional changes. These DVFs then guide a reconstruction pipeline that corrects motion on a perprojection basis by warping each back-projection. Experiments on phantom and clinical data demonstrate that this approach effectively corrects motion artifacts, yields superior reconstruction quality. Our framework yields high-quality static 3D images and enables full 4D-CBCT synthesis, paving the way for advanced adaptive radiotherapy workflows.
Motivation and Contributions
Iterative methods are too slow for clinical workflows.
✔ A Non-Iterative, Projection-Driven Framework.
Prior-based methods lack robustness to anatomical changes.
✔ A Decoupled, Patient-Specific Motion Model.
Conventional 4D-CBCT suffers from quality degradation.
✔ High-Fidelity, Full 4D-CBCT Synthesis.
Methods
(a) Offline Training: Learning a Patient-Specific Motion Model
Data Generation: We leverage a prior 4D-CT scan to generate a large-scale, augmented training dataset. Inter-phase deformations are combined with Thin-Plate Spline (TPS) warps to simulate a wide range of respiratory motions and anatomical variations.;
The PVD-Net is trained patient-specifically to predict the DVF that warps a moving CT volume to match a reference projection.
(b) Online Reconstruction: Synthesize a high-quality, motion-free 3D-CBCT.
For each new projection, the pre-trained PVD-Net rapidly infers its DVF (Φt). This DVF then guides a modified back-projection process.
Conventional FDK simply averages all projections, leading to motion blur:
Our Motion-Compensated FDK (MC-FDK) replaces the standard back-projector B with a dynamic, DVF-warped operator BMC:
The BMC operator uses the predicted DVF (Φt) to warp the back-projected volume and apply a density correction, effectively undoing the motion for each projection angle:
Experiments
Our framework accurately reconstructs the contemporary shrunken tumor (red arrow) despite guidance from an outdated prior with a larger tumor, demonstrating high robustness.
Our method's reconstruction ("Ours") shows superior visual quality, closely matching the ground-truth. The corresponding voxel-wise HU error map ("Ours") is substantially cleaner and closer to zero, indicating significantly higher accuracy compared to baseline methods which exhibit large, structured residual errors.
1. Robustness to Anatomical Changes
2. Superior Reconstruction Quality
3. High-Fidelity 4D-CBCT Synthesis
The proposed method generates high-quality reconstructions across the entire respiratory cycle (Phases 1, 5, and 10 shown), enabling full 4D-CBCT synthesis.
Also as shown in the table, our method consistently achieves the highest PSNR/SSIM and lowest RMSE across all evaluated respiratory phases (1, 5, 10). This stable, superior performance throughout the breathing cycle validates our framework's capability to synthesize complete and high-fidelity 4D-CBCT datasets.
Conclusion
CMMCA
Workshop